CHARACTERIZATION OF THE HUMMING-TYPE NOISE AND VIBRATION OF THE AUTOMOTIVE HVAC SYSTEM

A. Z. A. Mazlan1*, M. H. Hamdan1, M. S. Md. Isa1, S. Man2, M. A. R. Paiman2 and M. Z. Abd. Ghapar2

1TheVibrationLab, 
School of Mechanical Engineering, 
Universiti Sains Malaysia,

*Email: zhafran@usm.my

Phone: +6045996368; Fax: +6045996912

2Vehicle Comfort, Testing & Development, 
Vehicle Development & Engineering,

Proton Holdings Berhad.

ABSTRACT

There are various types of noise that can be induced from the effect of vibration of the automotive heating and ventilating air conditional (HVAC) system such as humming, hissing, clicking and air rush noises. These noises have to be characterizing properly in order to determine the root cause of each of the noise. In this study, the humming-type noise is taken into consideration whereby the noise and vibration characteristics are measured from various HVAC components such as power steering pump, compressor and air conditional pipe. Three types of measurement sensors are used in this study which is tachometer for the rpm tracking, accelerometer for the vibration and microphone for the noise measurement. Two types of operating condition are taken into consideration which is in idle (850 rpm) and running (850-1400 rpm) conditions and a constant blower speed is applied for both conditions. The result shows that the humming noises are determined at the frequency range of 300-350 Hz and 150-250 Hz for the both idle and running conditions, respectively. The vibration of the power steering pump shows the worst acceleration of 1.8 m/s2 at the frequency range of 150-250 Hz compared to the compressor and air conditional pipe. This result is validated with the 3D color order analysis whereby the humming noise color mapping shows the dominant result in this frequency range.

Keywords: Humming noise, HVAC system, vibration, rpm tracking and power steering pump.